## Slide 1: A Grid execution model for the ANSYS engineering simulation software
Alessandro COSTANTINI1, Marco BENCIVENNI1, Diego MICHELOTTO1, Daniele CESINI1, Emidio GIORGIO1, Luciano GAIDO1, Alberto MONETTI2, Mattia MANZOLARO2, Alberto ANDRIGHETTO2
1 INFN/IGI, Viale Berti Pichat 6/2, Bologna (IT)
2 INFN-LNL, Padova (IT)
alessandro.costantini@cnaf.infn.it

## Slide 2: Summary
European Grid Initiative and IGI
The User Community: SPES@INFN
The computational problem
Code Porting: ANSYS
License handling
A smart solution: IGI web portal
Conclusions

## Slide 3
Train users to use the new execution procedure
Disseminate the work done to find new applications for long term sustainability
Seek, identify, and closely support new communities to deploy their applications and create the computing model
Work-plan for application porting
The NGI_IT
User
Support and
Formation
(FUS) team

## Slide 4
The SPES project
SPES (Selective Production of Exotic Species) is a multi user project aimed at developing a Radioactive Ion Beam (RIB) facility covering interdisciplinary applied physics in the fields of material science and medical applications.
SPES is a project of the INFN Road Map for the Nuclear Physics development
  @ INFN Legnaro National Laboratories, Italy
  Research focused on the electro-thermal design of high temperature devices for the production of Radioactive Ion Beams

## Slide 5
The SPES project at LNL
Facility layout
Existing Piave-Alpi building
ISOL FACILITY
INTERDISCIPLINARY APLLICATIONS FACILITY
SPES Area

## Slide 6
Breeder
ISOL facility scheme

## Slide 7
The scientific problem
Simulation modeling of a real experimental machinery apparatus
Target: evaluate the stability and the mechanical strength
Software used: ANSYS simulation suite

## Slide 8: ANSYS simulation software
ANSYS suite is an engineering simulation software (computer-aided engineering, or CAE)
Offers a comprehensive range of engineering simulation solution sets (automotive, aerospace, energy, …)
Simulation Technology: Structural Mechanics, Multiphysics, Fluid Dynamics, Explicit Dynamics, Electromagnetics, Hydrodynamics
ANSYS offers different options for distributing model-solving power using multiple processors by using an embedded MPI communication layer

## Slide 9
Chart: heater current (A)
| 600.0 | 700.0 | 800.0 | 900.0 | 1000.0 | 1100.0 | 1200.0 | 1300.0
FEM | 1150 | 1277 | 1396 | 1508.55 | 1615 | 1717 | 1814 | 1908
EXP | 1147 | 1286 | 1417 | 1528 | 1627 | 1718 | 1795 | 1876
I =1300 A
P = 9 kW
Tin = 1850 °C
P = 9 kW !
Tout = 30 °C
Pyrometer
FEM model
ANSYS calculation for the
SPES project
Notes: 12/09/12
9

## Slide 10
1) Elettro-termo-struttural of the (Isolde) and (Hribf) FEBIAD
2) Comparison focused toward the new SPES FEBIAD
4) Study of the magnetic field using FEM
3) Validation of the FEM model
Ansys calculation for the
SPES project
Notes: 12/09/12
10

## Slide 11: The computational problem
ANSYS calculations performed by SPES can be treated as a series of independent computations
They require:
  A set of multiprocessors (or multicore) resources
  From hours to days of CPU time per computation
  Storage area to save the results coming from the computations (few GB/calculation)

## Slide 12: Application porting
ANSYS has been installed and configured in some Worker Nodes (WN) that belongs to the IGI domain, in a site located at CNAF on servers owned by the INFN
Both the installation and configuration have been carried out
  Under Scientific Linux 5.7 O.S.
  Using CLI procedures
WNs are accessed via batch system such as PBS or LSF

## Slide 13: License handling
25 Research licenses shared among different INFN owners
WNs are located close (on the same site) of the Flex server (due to license restrictions)
WNs can be accessed only by INFN owners of the license
License handling mechanism has been presented to the Italian dealer for approval
Work in progress to implement a monitor usage mechanism

## Slide 14
Computing Element (CE)
Site BDII (sBDII)
Batch System (PBS,LSF…)
Storage Element (SE)
Worker Nodes (WN)
Storage
ANSYS
UI
Personal Certficate
GROUP:
/GRIDIT/ANSYS
VOMS SERVER
FLEX SERVER
Access to the resources

## Slide 15: The IGI Portal facility
IGI Portal is a powerful and easy to use gateway to access distributed computing and storage resources
  Based on the WS-PGRADE application
  The generic application structure is a workflow
  Interface can be customized to support different user communities needs (GRIDIT, THEOPHYS, COMPCHEM, …)
A web GUI has been provided through a dedicated portlet
  To access the standard functionalities of the Grid
  To minimize the skills needed by the user to use the Infrastructure
IGI PORTAL Presentation
  xxx

## Slide 16: The typical usecase
User provides the initial input files and configuration parameters and waits for the results until the calculation is terminated
  APDL (collection of ANSYS commands)
  Input data
Needs
  Several days of computations
  Store GB of data for each computation
  Check the consistency of the output at runtime

## Slide 17: The ANSYS portlet

## Slide 18: The adopted solutions
The evolution's audit
A crucial aspect of such long time simulations is the evolution's audit of the calculations at runtime
Use has been made of the SRM-Client functionalities that exploit Grid Storage Elements
  temporary files and partial output are copied to the SE and made available for inspection at runtime
Exploiting the web-based features of the SRM-Server on the SE
  All the files stored in the SE (temporary and permanent) can be accessed via web

## Slide 19: The adopted solutions

## Slide 20: The adopted solutions
The computation time
Granted amount of CPU time is limited on Grid sites
  From 6 hours to few days
Specialized script developed to handle the checkpoint of the calculation
  set the computational environment needed for the application
  monitor the computation time allowing a safely interruption of the application
The user have to submit a new calculation to continue his/her work if the granted CPU time is not enough

## Slide 21: A step forward
Added value: the automatic workflow
The constantly grow of needs of the SPES community motivated us to develop a first prototypical workflow
  Portlet and script work in a collaborative way to implement a complex SPES usecase
  The workflow steps are conditioned by event-related dependences occurring at runtime

## Slide 22: Conclusion
ANSYS was successfully ported to Grid services in strong partnership with the SPES community in order to address their requirements
To preserve license restrictions a strict control on access was implemented through Grid services
The adoption of a “web based ad-hoc solution” allows also inexperienced users to execute ANSYS on the Grid
Work in progress to build a solid platform, offered to users as a service, for assembling accurate multi scale realistic simulations and workflows
  Implementation of a monitor usage mechanism